## Slide 1: MCP79410 Hours Alarm Issue
2024 SEP
Amond Lin

## Slide 2: Background
Application: Battery Life Calculation
  Using MCP79410 hours alarm output function to turn on the VDD power circuit of the external MCU, and only the RTC chip is powered continuity.
  Once the MCU is powered up, the MCU will read the ALM0HOUR and then write back with decreasing by 1. And the 23-hour alarm counter of MCU would be increased 1.
  So, the MCU would be powered up every 23 hours triggered by MCP79410 RTC alarm output function.
  Once 23-hour alarm counter reaches max value (~5 years), it means battery is end of live.

## Slide 3: Initialization
RTCSEC=0x00
RTCMIN=0x00
RTCHOUR=0x13
RTCWKDAY=0x0B
RTCDATE=0x22
RTCMTH=0x06
RTCYEAR=0x22
CONTROL=0x10
RTCSEC=0x80
ALM0SEC=0x00
ALM0MIN=0x00
ALM0HOUR=0x00
ALM0WKDAY=0x23
Hour match

## Slide 4: Right after production & Normal operation
1st step of their production SOP was to configure RTC based on present date & time and to configure 1st Alarm time with 0:00.
Once the 1st alarm occurred, ALM0HOUR would be read and written back with decreasing 1.
And then so on, the procedure would repeat every 23 hours.

## Slide 5: Failure Description
For example with above initial settings,
  MCP79410 RTC alarm output function would occur when RTCHOUR counted to 0x21 (ALM0HOUR = 0x21).
  At the moment, the MCU would be powered up and read the ALM0HOUR (= 0x21) and then write back with 0x20.
  It was expected to get alarm again after 23 hours, but the failure chips would alarm the system just after one hour (RTCHOUR=0x22) and then alarm the system again after 23 hours RTCHOUR=0x20).
  There should be only one-time alarm in 23 hours, but there were 2 times recorded.
Additional information:
  The failure rate was about 20% so far.
  One of failure chip:
    Microchip MCP79410-I/ST
    Track code.7941
    Date: I307 (Y2023, 07W)​
  The host MCU: dsPIC33CK128MP206

## Slide 6: Failure Analysis (Based on data packet from client)
Design operation
  Initialized date/time with present date/time (2022, JUN, 22, Wednesday, 13:00:00)
  Configure 1st Alarm time at 0:00.
  When ST(RTCSEC bit <7>)=1, RTCC would start working.
  When hour-match at 00:00:00, ALM0IF=1, MCU would config ALM0HOUR=0x23 and clear ALM0IF.
  When next time with ALM0IF=1, MCU would be powered up to read and write back ALM0HOUR (with decreasing 1) and then clear ALM0IF. And so on, the procedure would be expected with repeating every 23 hours.

## Slide 7: Time-line：Design operation
2022/6/22
WED
13:00:00
Set
00:00:00
RTCC
Alarm
2022/6/23
TUE
00:00:00
Set
23:00:00
2022/6/23
TUE
23:00:00
Set
22:00:00
2022/6/24
FRI
22:00:00
Set
21:00:00
2022/6/25
SAT
21:00:00
Set
20:00:00

## Slide 8: Failure Analysis (Based on data packet from client)
The problem:
  Initialized date/time with present date/time (2022, JUN, 22, Wednesday, 13:00:00)
  Configure 1st Alarm time at 0:00.
  When ST(RTCSEC bit <7>)=1，RTCC would start working.
  When hour-match at 00:00:00，ALM0IF=1.
  MCU would config ALM0HOUR=0x23 and clear ALM0IF.
  It was expected to get next alarm (let’s call 2nd alarm) after 23 hours, but 2nd aleam would occur again after only 1 hour (RTCHOUR=0x01). MCU didn’t know that, so MCU read and wrote back ALM0HOUR (0x23-1=0x22) again and clear ALM0IF.
  3rd alarm would occur properly after 23 hours.
  4th alarm would occur after only hour again.
  5th alarm would occur properly after 23 hours.
  6th alarm would occur after only hour again.
  And so so…until MCP79410 was power-down.

## Slide 9: Time-line：The problem
2022/6/22
WED
13:00:00
Set
00:00:00
RTCC
Alarm
2022/6/23
TUE
00:00:00
Set
23:00:00
2022/6/23
TUE
01:00:00
Set
22:00:00
2022/6/23
TUE
22:00:00
Set
21:00:00
2022/6/23
TUE
23:00:00
Set
20:00:00
2022/6/24
FRI
20:00:00
Set
19:00:00
2022/6/24
FRI
21:00:00
Set
18:00:00
2022/6/25
SAT
18:00:00
Set
17:00:00
Wrong Alarm
Wrong Alarm
Wrong Alarm

## Slide 10: Sept-20, 2024
Reported by Weikeng Amond Lin
All tests were based on Weikeng’s test environment and conditions.

## Slide 11: Test process
Initializations:
  RTCSEC=0x00
  RTCMIN=0x00
  RTCHOUR=0x05
  RTCWKDAY=0x03
  RTCDATE=0x18
  RTCMTH=0x09
  RTCYEAR=0x24
  CONTROL=0x14
  ALM0SEC=0x00
  ALM0MIN=0x00
  ALM0HOUR=0x10
  ALM0WKDAY=0x20
  RTCSEC=0x80

## Slide 12: Test process
dsPIC33CK256MP506 would check MCP79410 one time once MFP pin triggered MCU.
To speed up issue reproduction
  0x07H: CRSTRIM = 1
  0x08H: OSCTRIM=0xFF
  ~10mins in real world would be about 23 hours of RTCC.

## Slide 13: Data packet (Duplicated on EVM, not from client)
封包 | 名稱 | 起始點 | Start | Address | Write | A-ACK | Data | D-ACK |  |  | 
1 | Bus1(I2C) | 3.89079ms | Start | 6F | Write | A-ACK | 07 | D-ACK |  |  | 
2 | Bus1(I2C) | 4.09025ms | Start | 6F | Read | A-ACK | 14 | D-NACK | Stop | Master NACK | 
3 | Bus1(I2C) | 6.28412ms | Start | 6F | Write | A-ACK | 0C | D-ACK |  |  | 
4 | Bus1(I2C) | 6.48357ms | Start | 6F | Read | A-ACK | 10 | D-NACK | Stop | Master NACK | 
5 | Bus1(I2C) | 13.25091ms | Start | 6F | Write | A-ACK | 0C | D-ACK | 09 | D-ACK | Stop
6 | Bus1(I2C) | 14.26477ms | Start | 6F | Write | A-ACK | 0D | D-ACK |  |  | 
7 | Bus1(I2C) | 14.46427ms | Start | 6F | Read | A-ACK | 28 | D-NACK | Stop | Master NACK | 
8 | Bus1(I2C) | 21.406ms | Start | 6F | Write | A-ACK | 0D | D-ACK | 20 | D-ACK | Stop
9 | Bus1(I2C) | 22.41982ms | Start | 6F | Write | A-ACK | 07 | D-ACK |  |  | 
10 | Bus1(I2C) | 22.61933ms | Start | 6F | Read | A-ACK | 14 | D-NACK | Stop | Master NACK | 
11 | Bus1(I2C) | 28.95579ms | Start | 6F | Write | A-ACK | 00 | D-ACK |  |  | 
12 | Bus1(I2C) | 29.15526ms | Start | 6F | Read | A-ACK | 83 | D-NACK | Stop | Master NACK | 
13 | Bus1(I2C) | 29.97238ms | Start | 6F | Write | A-ACK | 01 | D-ACK |  |  | 
14 | Bus1(I2C) | 30.17176ms | Start | 6F | Read | A-ACK | 00 | D-NACK | Stop | Master NACK | 
15 | Bus1(I2C) | 30.98901ms | Start | 6F | Write | A-ACK | 02 | D-ACK |  |  | 
16 | Bus1(I2C) | 31.18843ms | Start | 6F | Read | A-ACK | 10 | D-NACK | Stop | Master NACK | 
17 | Bus1(I2C) | 32.0057ms | Start | 6F | Write | A-ACK | 03 | D-ACK |  |  | 
18 | Bus1(I2C) | 32.20512ms | Start | 6F | Read | A-ACK | 23 | D-NACK | Stop | Master NACK | 
19 | Bus1(I2C) | 33.02315ms | Start | 6F | Write | A-ACK | 04 | D-ACK |  |  | 
20 | Bus1(I2C) | 33.22271ms | Start | 6F | Read | A-ACK | 18 | D-NACK | Stop | Master NACK | 
21 | Bus1(I2C) | 34.03961ms | Start | 6F | Write | A-ACK | 05 | D-ACK |  |  | 
22 | Bus1(I2C) | 34.23898ms | Start | 6F | Read | A-ACK | 29 | D-NACK | Stop | Master NACK | 
23 | Bus1(I2C) | 35.05597ms | Start | 6F | Write | A-ACK | 06 | D-ACK |  |  | 
24 | Bus1(I2C) | 35.25542ms | Start | 6F | Read | A-ACK | 24 | D-NACK | Stop | Master NACK | 
25 | Bus1(I2C) | 44.00665ms | Start | 6F | Write | A-ACK | 0C | D-ACK |  |  | 
26 | Bus1(I2C) | 44.20609ms | Start | 6F | Read | A-ACK | 09 | D-NACK | Stop | Master NACK | 
27 | Bus1(I2C) | 46.48592ms | Start | 6F | Write | A-ACK | 0D | D-ACK |  |  | 
28 | Bus1(I2C) | 46.68535ms | Start | 6F | Read | A-ACK | 20 | D-NACK | Stop | Master NACK | 

## Slide 14: Read/Write with UART print info
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
7
8
9

## Slide 15: Data packet timing

## Slide 16: Sept-22, 2024
Reported by Weikeng Amond Lin
All tests were based on Weikeng’s test environment and conditions.

## Slide 17: Typo – Update p.12
P.12
  0x07H: CRSTRIM = 1
  0x08H: OSCTRIM=0xFF

## Slide 18: Additional Feedback from client
MCU would config CRSTRIM = 0 by byte-writing during initialization.
OSCTRIM was never configured by MCU during/after initialization.

## Slide 19: Additional Feedback from client
I2C speed: 100K with 3.3V Vdd
I2C AC CHARACTERISTICS
  Measured Tr = 450ns

## Slide 20: Question from Weikeng to client
Q: Once ALM0IF was cleared, MFP would be pull-high immediately. Was the last frame sent completely before MCU was off?
Ans:
  Client will compare the last frame timing with MFP pin.

## Slide 21: Sept-23, 2024
Reported by Weikeng Amond Lin
All tests were based on Weikeng’s test environment and conditions.

## Slide 22: Timing sequence from client (1/3)
VCC would start falling down after 955ns with MFP pull-high.

## Slide 23: Timing sequence from client (2/3)
When VCC was powered down (RTC got to sleep), VCC down from 1.7V to 1.3V would take about 14ms to compare with T15 on data sheet.

## Slide 24: Timing sequence from client (3/3)
When RTCC waked up, MFP was low. Right after 14ms, VCC started going up from 0~3.3V to compare with T16 on datasheet.

## Slide 25: Test process
Initializations:

## Slide 26: Test process 2
Calibration process
  repeat read those register 14 times
    ALM0WKDAY, RTCWKDAY, RTCSEC, RTCMIN, RTCHOUR, RTCDATE, RTCMTH, RTCYEAR, CONTROL, ALM0HOUR, ALM0MIN, ALM0SEC
  Initial the following register in order
    RTCSEC=0x30, ALM0WKDAY=0x22, ALM0SEC=0x00, ALM0MIN=0x00, ALM0HOUR=0x00, CONTROL=0x14, OSCTRIM=0xFF, RTCYEAR=0x23, RTCMTH=0x09, RTCDATE=0x18, RTCHOUR=0x16, RTCMIN=0x06, RTCWKDAY=0x0A, RTCSEC=0xB0
Power on sequence
  We programed the MCU and then disconnected the USB cable. Once VDD of the MCU and RTCC dropped to zero, the USB cable was connected again to check the initial flow.

## Slide 27: Calibration Flowchart
MCU
Initial
count=13
Read RTCC
Initial RTCC
Read RTCC
Write
RTCWKDAY=0x29
count=8
ALM0IF=1
Wait Alarm
Read ALM0HOUR
Write ALM0HOUR -= 1
ALM0IF = 0
Y
N
N
Y
Y
N

## Slide 28: Need to check
After RTCC initial and set ST bit(RTCSEC<Bit 7>)
RTCWKDAY = 0x0A
Upon reading the RTCC for the second time, we wrote RTCWKDAY=0x29 and found that ALM0IF had been set.
Only read for check PWRFAIL and write back, not modify value.

## Slide 29: Sept-24, 2024
Reported by Weikeng Amond Lin
All tests were based on Weikeng’s test environment and conditions.

## Slide 30: Calibration Flowchart：Modified to match actual process
MCU
Initial
count=13
Read RTCC
Initial RTCC
Read RTCC
Read and write back
RTCWKDAY
count=8
ALM0IF=1
Wait Alarm
Read ALM0HOUR
Write ALM0HOUR -= 1
ALM0IF = 0
Y
N
N
Y
Y
N
Reset count >= 4
Y
N
MCU
Reset

## Slide 31: Teraterm Log

## Slide 32: Question from Weikeng to client
With the failure chip on power unit, can we see the same situation after initializing the RTCC?

## Slide 33: Sept-25, 2024
Reported by Weikeng Amond Lin
All tests were based on Weikeng’s test environment and conditions.

## Slide 34: Production process with RTCC, without MCU.
Step1. Battery assembly
Main Board
with RTCC
Battery
RTCC
VBAT
Main Board
with RTCC
Battery
RTCC
VBAT
Step3. RTCC Calibration Process
test fixture
Main Board
with RTCC
Battery
RTCC
VBAT
Step2. Charging Station
Production Steps
VCC

## Slide 35: Final test process with RTCC & MCU.
Step1. Battery assembly
Main Board
with RTCC
Battery
RTCC
VBAT
Main Board
with RTCC
Battery
RTCC
VBAT
Step3. RTCC Calibration Process
test fixture
Main Board
with RTCC
Battery
RTCC
VBAT
Step2. Charging Station
Production Steps
VCC
Main Board
with RTCC
Battery
RTCC
VBAT
VCC
MCU
Execute
calibration
Final test Process
(Normally)
Once MFP=1
Main Board
with RTCC
Battery
RTCC
VBAT
VCC
MCU
Read &
write back
If no **issue was detected for 3 times (MFP=1 for 3 tims), MCU would do 1 time RTCC calibration and then back to hour-alarm mode.
RTCC Calibration Process
*RTCC was never power-off.
什麼意思?
**Issus means RTCHOUR != ALM0HOUR was detected but MFP=1.

## Slide 36: Final test process with RTCC & MCU.
Step1. Battery assembly
Main Board
with RTCC
Battery
RTCC
VBAT
Main Board
with RTCC
Battery
RTCC
VBAT
Step3. RTCC Calibration Process
test fixture
Main Board
with RTCC
Battery
RTCC
VBAT
Step2. Charging Station
Production Steps
VCC
Main Board
with RTCC
Battery
RTCC
VBAT
VCC
MCU
Execute
calibration
Final test Process
(with **issue)
Once MFP=1
Main Board
with RTCC
Battery
RTCC
VBAT
VCC
MCU
Read &
write back
If **issue was detected, MCU would not do RTCC calibration and keep in hour-alarm mode.
RTCC Calibration Process
*RTCC was never power-off.
什麼意思?
**Issus means RTCHOUR != ALM0HOUR was detected but MFP=1.

## Slide 37: Question from BU to field
Question: If a chip fails as per the PPT (some even-numbered hours fail in 24 Hour mode), can a failed hour be repeated immediately? That is, if the fail at hour 22:00 is repeated again, does it fail again?
  Ans: Before RTCC is power-off, the issue would continue repeating and never stop. 22:00 was just one of examples. It could be any other hour. Additional update:
    RTCC was always powered by battery and was never power-off.
    The issue can be only reproduced with two conditions so far as we known:
      Reproducible ONLY on client’s product main board. (we have not been able to reproduce the issue on EVM.)
      The failure chip can NOT be re-initialized again after “Production Steps”. Re-initialization means the step3 of production steps. If did that again, the issue would not happen …at least we didn’t see the issue again with the same failure chip and unit.

## Slide 38: Question from BU to field
Question: Need to get some failed units to help confirm this issue.?
  Ans: Most failure units are still in factory. Will check with client for the failure units. On the other hands, Weikeng Amond has 1 failure chip but has not been able to reproduce the issue on our EVM.

## Slide 39: Thanks.

## Slide 40: RTCC assemble and Test process
Main Board
with RTCC
Battery
RTCC
VBAT
VCC
MCU
run calibration
Battery assembly
Main Board
with RTCC
Battery
RTCC
VBAT
Main Board
with RTCC
Battery
RTCC
VBAT
Calibration Process
test fixture
Main Board
with RTCC
Battery
RTCC
VBAT
Charging Station
Production Line
VCC
Test Process
MFP=1
Main Board
with RTCC
Battery
RTCC
VBAT
VCC
MCU
Read and write back
x3 times
Calibration Process
when RTCHOUR != ALM0HOUR
determined to be a failed